### How to Flash and Upload Code to ATtiny85 (HW-260 USB Board) Using an Arduino UNO and Micronucleus
This guide provides step-by-step instructions to burn the correct bootloader and upload a Blink sketch to an ATtiny85-based HW-260 USB board using an Arduino UNO as a programmer and Micronucleus CLI.

## 1. Burn the Micronucleus Bootloader to ATtiny85 Using Arduino UNO
### 1.1. Set Up the Arduino UNO as an ISP Programmer
1. Connect the Arduino UNO to your PC and open Arduino IDE 2.0.
2. Go to: File > Examples > 11. ArduinoISP > ArduinoISP.
3. Select the Board: Arduino UNO (Tools > Board > Arduino AVR Boards > Arduino UNO).
4. Select the Port: Check Tools > Port and select the Arduino UNO port.
5. Upload the ArduinoISP sketch to the UNO.

### 1.2. Wire the Arduino UNO to the ATtiny85
Use the following wiring to connect the ATtiny85 to the Arduino UNO:

💡 Tip: Add a 10µF capacitor between RESET and GND on the Arduino UNO to prevent it from resetting. (Ou um 223 cerâmico também serviu).

### 1.3. Burn the Micronucleus Bootloader
1. Open Arduino IDE 2.0.
2. Go to Tools > Board > ATtiny85 (if not installed, install ATtinyCore).
3. Set the following settings:
  1. Chip: ATtiny85
  2. Clock: 16.5 MHz (Digispark - Default)
  3. Programmer: Arduino as ISP
4. Burn the bootloader by running:
  avrdude -c stk500v1 -b 19200 -P /dev/ttyACM0 -p t85 -U flash:w:t85_default.hex -U lfuse:w:0xe1:m -U hfuse:w:0xdd:m -U efuse:w:0xfe:m
https://github.com/micronucleus/micronucleus/blob/master/firmware/releases/t85_default.hex
  1. Replace /dev/ttyACM0 with the correct port of your Arduino UNO.

## 2. Install Micronucleus for Uploading Code via USB
### 2.1. Install Dependencies
Run the following in a terminal:
sudo apt update
sudo apt install git libusb-dev
### 2.2. Download and Install Micronucleus
git clone https://github.com/micronucleus/micronucleus.git
cd micronucleus/commandline
make
sudo make install
### 2.3. Verify Installation
micronucleus --help
If installed correctly, it will display usage instructions.

## 3. Upload the Blink Sketch to ATtiny85
### 3.1. Write the Blink Sketch
Since LED_BUILTIN is not defined for Digispark boards, use pin 1 explicitly:
const int LED_PIN = 1; // Use ATtiny85 Pin 1 (PB1)

void setup() {
    pinMode(LED_PIN, OUTPUT);
}

void loop() {
    digitalWrite(LED_PIN, HIGH);
    delay(1000);
    digitalWrite(LED_PIN, LOW);
    delay(1000);
}

### 3.2. Compile and Extract the .hex File
1. Enable verbose output in Arduino IDE:
  1. Go to: File > Preferences.
  2. Check: "Show verbose output during compilation".
2. Click "Verify" (✔️ button) to compile.
3. Find the .hex file path in the output log:
  /tmp/arduino_build_123456/Blink.ino.hex
4. Copy the .hex file to a safe location:
  cp /tmp/arduino_build_123456/Blink.ino.hex ~/blink.hex

### 3.3. Upload the .hex File to ATtiny85 Using Micronucleus
1. Plug in the ATtiny85 USB Board.
2. Run the upload command:
  micronucleus --run ~/blink.hex
3. When prompted, unplug and replug the ATtiny85 USB Board.
4. Wait for the upload to complete.

## 4. Troubleshooting
- No USB detection?
  dmesg | tail -20
  - Use USB 2.0 ports (some USB 3.0 ports don’t work well).
  - Try using a powered USB hub.
- Permission issues? Run:
  sudo micronucleus --run ~/blink.hex
- Arduino IDE not recognizing Digispark?
  - Reinstall the Digistump AVR package:
    arduino-cli core install digistump:avr

## Final Notes
🎯 You should now see the LED on pin 1 blinking!
This guide ensures you can burn the bootloader, compile, and upload firmware to your ATtiny85 board using Micronucleus. 🚀
Let me know if you need further clarifications!

----

const int LED_PIN = 1; // Define LED pin as constant

void setup() {
    pinMode(LED_PIN, OUTPUT); // Set pin 1 as output
}

void loop() {
    digitalWrite(LED_PIN, HIGH); // Turn LED on
    delay(1000);
    digitalWrite(LED_PIN, LOW); // Turn LED off
    delay(1000);
}