### How to Flash and Upload Code to ATtiny85 (HW-260 USB Board) Using an Arduino UNO and Micronucleus
This guide provides step-by-step instructions to burn the correct bootloader and upload a Blink sketch to an ATtiny85-based HW-260 USB board using an Arduino UNO as a programmer and Micronucleus CLI.

## 1. Burn the Micronucleus Bootloader to ATtiny85 Using Arduino UNO
### 1.1. Set Up the Arduino UNO as an ISP Programmer
1. Connect the Arduino UNO to your PC and open Arduino IDE 2.0.
2. Go to: File > Examples > 11. ArduinoISP > ArduinoISP.
3. Select the Board: Arduino UNO (Tools > Board > Arduino AVR Boards > Arduino UNO).
4. Select the Port: Check Tools > Port and select the Arduino UNO port.
5. Upload the ArduinoISP sketch to the UNO.

### 1.2. Wire the Arduino UNO to the ATtiny85
Use the following wiring to connect the ATtiny85 to the Arduino UNO:

💡 Tip: Add a 10µF capacitor between RESET and GND on the Arduino UNO to prevent it from resetting. (Ou um 223 cerâmico também serviu).

### 1.3. Burn the program hex using Arduino UNO as ISP:
avrdude -c stk500v1 -b 19200 -P /dev/ttyACM0 -p t85 -U flash:w:/home/milhas/.var/app/cc.arduino.IDE2/cache/arduino/sketches/A590DD0DB7006373D259ECE8839E819F/key.ino.hex -U lfuse:w:0xe1:m -U hfuse:w:0xdd:m -U efuse:w:0xfe:m
  1. Replace /dev/ttyACM0 with the correct port of your Arduino UNO.

----

const int LED_PIN = 1; // Define LED pin as constant

void setup() {
    pinMode(LED_PIN, OUTPUT); // Set pin 1 as output
}

void loop() {
    digitalWrite(LED_PIN, HIGH); // Turn LED on
    delay(1000);
    digitalWrite(LED_PIN, LOW); // Turn LED off
    delay(1000);
}